## Slide 1: Low-Maintenance, Affordable Dual Bucket Worm Composter
Pictured above: Indoor/Outdoor Dual Bucket Worm Composter
A Solution for Urban/Suburban Composting

## Slide 2: Background
I have been using vermicomposting (worm composting) for over 20 years.
Initially I purchased and used a multi-tray composter and then built my own multi-level bin composter; neither was truly satisfactory.
The problems with these vermicomposters was the build up of moisture and leachate, which slowed compost formation and increased the presence of pests.
Another issue was the aversion most people have with the idea of keeping worms inside their houses or dealing with them in any manner. (including my own family)
The system proposed in this presentation would permit year-round composting with minimal maintenance.

## Slide 3: Obstacles to Conventional Composting in Suburban Locations
Lack of space (average lot size in Fairfield, CT below I-95 is less than 0.15 acre)
Fear of attracting rodents or other pests
Lack of knowledge of composting and its benefits
Standard compost bins are smaller than the 1 cubic yard required to create and maintain the necessary thermophillic reaction and many do not function even under optimal conditions.
Time and physical effort needed to ‘turn’ compost pile on a timely basis.
A compost pile lies dormant for much of the late fall and winter, requiring alternative disposal of food waste.

## Slide 4: What is Vermicomposting (Worm Composting)
Vermicomposting is the practice of using earthworms to process vegetal food scraps into a highly valuable source of plant nutrients.
Unlike conventional composting which is thermophillic (requiring a heat generating bacterial process), vermicomposting is the product of earthworm activity, which employs a broad range of bacterial and worm digestive and physical processes .

## Slide 5: Differences Between Worm and Conventional Composting
Worm Composting
  Uses red wiggler earthworms and soil bacteria to process food scraps
  Can work with any quantity of material, depending on # of worms.
  Little maintenance to work effectively
  Can be used on plants upon completion of process
  Can be accomplished indoors
  Utilizes smaller quantities of more specific food waste and takes longer to complete the composting process.
Conventional Composting
  Needs thermophillic bacteria to breakdown material, usually yard waste.
  Requires at least 1 cu. yard of plant material to work effectively
  Requires frequent rotation to get entire pile engaged in active composting.
  Requires a ‘curing’ period prior to using compost as a soil amendment
  Best created outdoors
  Capable of processing large quantities of plant matter in a shorter period of time.

## Slide 6: Advantages of Worm Composting
Can be created indoors/outdoors year-round.
Requires little maintenance or attention
Yields superior fertilizer for plant growth not only in terms of nutrients but also in terms of increased plant pest resistance and reduced water demand.1
Acts as a plant growth stimulator as it is rich in plant growth hormones, humus and bio-available nutrients.1
Does not require the curing period of conventional compost; may be used immediately.

## Slide 7: Nutrient Comparisons Worm vs. Conventional Compost2

## Slide 8: Worm Compost Results Compared to Chemical Fertilizer and Conventional Compost in Potted Wheat Development6

## Slide 9: Strategy to Improve Adoption of Worm Composting
Barriers to Acceptance
Aversion to worms
Fear of worms escaping composter
Messy maintenance of most worm composters
Accumulation and disposal of worm compost leachate
Possibility of insect pests esp. fruit flies
Elements Needed for Acceptable Worm Composter
Prevent worms from escaping composter
Easy maintenance
Separate leachate from worm compost in an easily emptied container
Prevent insect pests from proliferating inside and outside of composter

## Slide 10: The Indoor/Outdoor Dual Bucket Worm Composter
The Indoor/Outdoor Dual Bucket Worm Composter provides a solution to the barriers to wider acceptance of composting.
A 3-gallon food-grade plastic (HDPE #2) rests inside a 5-gallon plastic bucket equipped with two, 2-inch screened vents (soffets).
The 2.5-gallon bucket is perforated at 2-3 inch intervals with a ¼ drill.
  A circle of window screening is placed on this bucket’s floor
  Two 1-inch vents are installed around the top of the bucket just below the lid
  The lid is secured tightly with a 10-inch bungee cord.
  It is secured to the 5-gallon bucket in a hole cut in its lid
Materials for the Dual Bucket Worm Composter can be purchased for under $15. Coir can be purchased for about $2 per 9 oz. brick. Red wiggler worms are available online for $15-$20 per 250 plus shipping.

## Slide 11: Dual Bucket Worm Composter
Complete dual bucket worm composter ready for indoor usage
Inner bucket in raised bed during growing season (note the shaded location)

## Slide 12: Indoor/Outdoor worm composter views
Inner bucket with vents and screening in base
Inner 2.5-gallon bucket above 5-gallon outer bucket

## Slide 13: Indoor/Outdoor Worm Composter in Winter Mode
Composter is placed on a seedling heat mat that can be activated in cold weather in a garage or power-equipped out-building.
A cloth cover is placed over the composter to retain heat which should keep the inner bucket between 65 -75° F on even the coldest days.
Composter may be employed throughout late fall, winter and early spring and finished worm compost may be retained in a separate container until spring soil preparation.

## Slide 14: Bucket Worm Composter Function
Inner bucket has a large population (200-300) of red wiggler worms for rapid processing of worm compost
Worms should be fed chopped (human bite size) vegetable/fruit scraps.
Prior to being placed in the worm composter, scraps should be secured in a 1 quart air-tight plastic container. This prevents insect pest (e.g. fruit flies) from laying eggs and infesting the composter.
Drain excess liquid from the food scraps container prior to emptying it in the composter. Spread the scraps in a uniform layer across the surface of its contents.
Cover each addition of food scraps with about 1/2 inch of hydrated coir (shredded coconut husk).
The inner bucket can be used outdoors, buried up to its vents, in a raised bed, facilitating the disposal of food scraps. This will keep any pest or odor issues outdoors with continuous leachate disposal.

## Slide 15: Worm Compost Leachate
Leachate is the dark liquid that drains to the bottom container of worm composters and is a combination of plant liquids and liquid runoff of the material and organisms in the composter. It can be rich in plant-available nutrients3 but tends to be anaerobic and can be a source of non-beneficial bacteria.
This liquid is not compost tea, which can only be created in aerobic conditions with finished compost and an effective aeration system.
Compost tea is extremely beneficial to plants, both as a soil and foliar additive, especially if actively aerated. Leachate may be added to a compost tea generator where the highly aerobic environment will neutralize any harmful bacteria.
The In-Ground Composter allows this liquid to drain into the subsoil where is can be utilized by soil micro-organisms and not adversely affect crops in the raised bed.

## Slide 16: Coir buffers compost moisture; it is pH neutral and can be consumed by worms
Dehydrated Coir – 9 0z. Block
Adding ½ gallon water creates 1 gallon plus of hydrated coir

## Slide 17: What Should/Should Not Be Added to a Worm Composter
Add These
Vegetable/Fruit Scraps
Pasta, Bread
Coffee Grounds
Shredded Newspaper
(Above recommendations designed to create finished worm compost as quickly as possible)
Do Not Add These
Meat/Meat by products
Dairy Products
Oils
Citrus
Hot Peppers
Thick rinds e.g watermelon
Thick skin shavings e.g. squash
Potato skins
Corn Cobs
Fruit pits, seeds
Thick Stems e.g. banana

## Slide 18: Size of Scraps Added
Not This: Remove stalks and fruit stickers
This: Cutting up scraps accelerates composting

## Slide 19: Setting Up the Worm Composter
Inner Bucket Setup
Place a minimum of 2 inches of hydrated coir in the base of the inner bucket.
Add 200-300 red wigglers in worm compost.
Cover the worms with at least an inch or two of hydrated coir
Add 1 quart of food scraps following advice on pages 13-14.
Alternate layers of coir and food scraps.
Worms will ascend, processing food scraps as they rise.
When bucket is full, remove the upper layers where most of the worms reside. Empty the remaining content on newspaper or plastic and return any stray worms to upper 1/3 portion.
Return the worms and unprocessed food scraps to the bucket; add coir as needed
Worm compost collected can be added to garden soil or used to create compost tea.
Repeat steps 3-6.
2 inches of Hydrated Coir
200-300 worms in WC
1 quart food scraps
1 inch Hydrated Coir
Alternating Layers of Food Scraps and Hydrated Coir

## Slide 20: Harvesting Worm Compost
As the inner bucket is filled with processing food scraps, further additions should be slowed to allow worms to complete their digestion.
The inner bucket should be removed from the outer bucket (or the soil) and the upper third set aside. The lower 2/3 should be emptied onto a plastic sheet.
Remove the worms and egg cocoons and place them with the upper third and return to the composter.
Repeat the additions of food scraps and coir until the next harvest.

## Slide 21: Worm Compost Harvested from an In-Ground Worm Composter
In-Ground Worm Composter and compost with worms removed
Close Up of Worm Compost

## Slide 22: Advantages of Worm Compost from In-Ground Composter
  Moisture of compost is regulated by soil itself; raised bed generally provide a warmer and slightly drier compost
  This drier compost is easier to spread on garden beds and allows easier incorporation into the root zone
  Tray and bin worm composters produce compost with a much higher moisture level which impedes incorporation into garden soils.

## Slide 23: Worm Compost Spread on a Raised Bed Prior to Incorporation into Root Zone
Raised bed has been cleared of previous crops
Worm compost is lighter brown material on the surface of darker raised bed soil
This bed has been mulched with straw and has had no foot traffic or cultivation to compact the soil.
Bed was covered with porous cloth and greenhouse plastic much of the year, ensuring optimal soil structure and weed prevention.
As a result of these measure, the added worm compost was incorporated into the soil with just a leaf rake, leaving most of the soil profile undisturbed.

## Slide 24: Benefits of Worm Compost Tea
Worm compost can be utilized to create compost tea, which may be as beneficial to plants as the compost itself
Aerated compost tea provides soil and plant surfaces with billions of beneficial microorganisms.
Worm compost tea, either as a foliar or soil application, can prevent plant diseases and improve plant growth and development4

## Slide 25: Brewing Compost Tea
Optimal Compost Tea Generation can be achieved with 1 pound of worm compost per 5 gallons of de-chlorinated water4.
Research indicates 0.8L/min. of air are required to keep compost tea actively aerated (>5 ppm dissolved 02)5
Dr. Elaine Hingham demonstrated that dissolved 02 levels below 6 ppm will decrease beneficial bacteria populations4
While research varies, actively aerated compost tea (AACT) requires about 48 hours of aeration in order to provide optimal micro-organism population and elimination of potential harmful anaerobic bacteria4.
Compost tea can be directly applied to soils and plants or at a 1:1 dilution with de-chlorinated water4.

## Slide 26: Basic Compost Tea Generator
This is a basic compost tea generator consisting of:
A 5 gallon food grade plastic bucket and lid
A high-volume air pump (this one is rated at 571 gallons/hour or 9.5 gallons/min)
A large bubble aerator (smaller bubbles in the 1mm range can injure beneficial microbes) which will aerate and agitate the mixture.
A porous, sealable, food-grade nylon bag that will hold up to 3 pounds of worm compost and hangs suspended in the bucket by an attached cord
The compost tea bucket is filled 4 gallons (to allow space for foaming which will occur) of de-chlorinated water obtained from a garden hose attached to a chlorine filter.
Aerator is run for a minimum of 48 hours to create optimal populations of beneficial aerobic bacteria and eliminate any anaerobic and facultative anaerobic bacteria.

## Slide 27: Summary
Worm Composting is an attractive alternative to conventional composting where space, knowledge and a commitment to maintain a compost pile are lacking.
Worm Compost and Compost Tea are superior amendments for plant growth, disease resistance and water retention.
Worm Composting requires less maintenance and can be used immediately upon its completion unlike conventional compost.
The Indoor/Outdoor Dual Bucket Worm Composter largely eliminated the barriers and concerns for those seeking to pursue composting.

## Slide 28: References
1 The Wonders of Earthworms & Its Vermicompost in Farm Production…, Agricultural Sciences Vol. 1, No. 2 2010
http://www.scirp.org/journal/PaperInformation.aspx?PaperID=2538
2 A Comparison Analysis of Vermicomposting Strategies in Food Substrates with an Emphasis on Nutrient Value and Reproduction, University of Wisconsin, Platteville
https://www.uwplatt.edu/files/urce/Lange.pdf
3 Potential of Vermicomposting Leachate as Organic Foliar Fertilizer and Nutrient Solution… 2012 2nd International Conference on Environment and BioScience IPCBEE vol.44 (2012)
http://www.ipcbee.com/vol44/010-ICEBS2012-F00019.pdf
4 The Compost Tea Brew Manual, 5th Edition, 2002 Elaine R. Hingham, PhD, p. 36
5 Effects of Aeration, Molasses, Kelp, Compost Type, And Carrot Juice on the Growth of Escherichia Coli in Compost Teas , Journal Compost Science & Utilization Volume 14, 2006 – 1
https://www.tandfonline.com/doi/abs/10.1080/1065657X.2006.10702261?src=recsys
6 Agronomic Impact Studies of Vermicompost vis-a-vis Conventional Compost & Chemical Fertilizer on Potted Wheat Crops (Griffith University, Brisbane, Australia 2008) Am-Euras. J. Agric. & Environ. Sci., 5 (S): 01-55, 2009